## Slide 1: NMEA PROTOCOL
Italian Maritime academy technology
Course: dp maintenance
Coacher: Ing. Stefano trivellini

## Slide 2: NMEA PROTOCOL
The National Marine Electronics Association (NMEA) is a non-profit association of manufacturers, distributors, dealers, educational institutions, and others interested in peripheral marine electronics occupations. The NMEA 0183 standard defines an electrical interface and data protocol for communications between marine instrumentation.
NMEA 0183 is a voluntary industry standard, first released in March of 1983. It has been updated from time to time; the latest release, currently (August 2001) Version 3.0, July 2001.

## Slide 3: NMEA PROTOCOL
NMEA has also established a working group to develop a new standard for data communications among shipboard electronic devices. The new standard, NMEA 2000, is a bi-directional, multi-transmitter, multi-receiver serial data network. It is multi-master and self-configuring, and there is no central controller.
The NMEA began a beta testing period in January 2000 with eleven manufacturers. A release version of NMEA 2000 is expected in 2001.

## Slide 4: NMEA PROTOCOL
NMEA 0183 devices are designated as either talkers or listeners (with some devices being both), employing an asynchronous serial interface with the following parameters:
Baud rate: 4800 bit/s
Number of data bits: 8 (bit 7 is 0)
Stop bits: 1 (or more)
Parity: none
Handshake: none

## Slide 5: NMEA PROTOCOL
NMEA 0183 allows a single talker and several listeners on one circuit. The recommended interconnect wiring is a shielded twisted pair, with the shield grounded only at the talker. The standard dos not specify the use of a particular connector. Note: The new 0183-HS standard (HS = high speed) introduced in version 3.0 uses a 3-wire interface and a baud rate of 38400. This type of interface is not discussed here.

## Slide 6: NMEA PROTOCOL
Its is recommended that the talker output comply with EIA RS-422, a differential system with two signal lines, "A" and "B". Differential drive signals have no reference to ground and are more immune to noise.
However, a single-ended line at TTL level is accepted as well. The voltages on the A line correspond to those on the TTL single wire, while the B voltages are inverted (when output A is at +5 V, output B is at 0 V, and vice versa. This is the unipolar RS-422 operation. In bipolar mode ±5 V are used).

## Slide 7: NMEA PROTOCOL
In either case, the recommended receive circuit uses an opto-isolator with suitable protection circuitry.
The input should be isolated from the receiver's ground. In practice, the single wire, or the RS-422 "A“ wire may be directly connected to a computer's RS-232 input. In fact even many of the latest products, like hand-held GPS receivers, do not have a RS-422 differential output, but just a single line with TTL or 5 V CMOS compatible signal level.

## Slide 8: NMEA PROTOCOL
General Sentence Format

## Slide 9: NMEA PROTOCOL
All data is transmitted in the form of sentences. Only printable ASCII characters are allowed, plus CR (carriage return) and LF (line feed). Each sentence starts with a "$" sign and ends with <CR><LF>. There are three basic kinds of sentences: talker sentences, proprietary sentences and query sentences.
Talker Sentences. The general format for a talker sentence is:
$ttsss,d1,d2,....<CR><LF>

## Slide 10: NMEA PROTOCOL
The first two letters following the „$” are the talker identifier.
The next three characters (sss) are the sentence identifier, followed by a number of data fields separated by commas, followed by an optional checksum, and terminated by carriage return/line feed. The data fields are uniquely defined for each sentence type. An example talker sentence is:
$HCHDM,238,M<CR><LF>
where "HC" specifies the talker as being a magnetic compass, the "HDM" specifies the magnetic heading message follows. The "238" is the heading value, and "M" designates the heading value as magnetic.

## Slide 11: NMEA PROTOCOL
A sentence may contain up to 80 characters plus "$“ and CR/LF. If data for a field is not available, the field is omitted, but the delimiting commas are still sent, with no space between them. The checksum field consists of a "*" and two hex digits representing the exclusive OR of all characters between, but not including, the "$" and "*".

## Slide 12: NMEA PROTOCOL
Proprietary Sentences. The standard allows individual manufacturers to define proprietary sentence formats.
These sentences start with "$P", then a 3 letter manufacturer ID, followed by whatever data the manufacturer wishes, following the general format of the standard sentences. Some proprietary sentences, mainly from Garmin, Inc., are listed in chapter 6.

## Slide 13: NMEA PROTOCOL
Query sentences. A query sentence is a means for a listener to request a particular sentence from a talker. The general format is:
$ttllQ,sss,[CR][LF]
The first two characters of the address field are the talker identifier of the requester and the next two characters are the talker identifier of the device being queried (listener). The fifth character is always a "Q“ defining the message as a query. The next field (sss) contains the three letter mnemonic of the sentence being requested. An example query sentence is:
$CCGPQ,GGA<CR><LF>
where the "CC" device (computer) is requesting from the "GP" device (a GPS unit) the "GGA" sentence. The GPS will then transmit this sentence once per second until a different query isrequested.

## Slide 14: NMEA PROTOCOL
Talker Identifiers
AG Autopilot - General
AP Autopilot - Magnetic
CD Communications – Digital Selective Calling (DSC)
CR Communications – Receiver / Beacon Receiver
CS Communications – Satellite
CT Communications – Radio-Telephone (MF/HF)
CV Communications – Radio-Telephone (VHF)
CX Communications – Scanning Receiver
DF Direction Finder
EC Electronic Chart Display & Information System (ECDIS)
EP Emergency Position Indicating Beacon (EPIRB)
ER Engine Room Monitoring Systems
GP Global Positioning System (GPS)
HC Heading – Magnetic Compass
HE Heading – North Seeking Gyro
HN Heading – Non North Seeking Gyro
II Integrated Instrumentation
IN Integrated Navigation
LC Loran C
P Proprietary Code
RA RADAR and/or ARPA
SD Sounder, Depth
SN Electronic Positioning System, other/general
SS Sounder, Scanning
TI Turn Rate Indicator
VD Velocity Sensor, Doppler, other/general
DM Velocity Sensor, Speed Log, Water, Magnetic
VW Velocity Sensor, Speed Log, Water, Mechanical
WI Weather Instruments
YX Transducer
ZA Timekeeper – Atomic Clock
ZC Timekeeper – Chronometer
ZQ Timekeeper – Quartz
ZV Timekeeper – Radio Update, WWV or WWVH

## Slide 15: NMEA PROTOCOL
Sentence Identifiers and Formats
GGA Global Positioning System Fix Data. Time, Position and fix related data
for a GPS receiver
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
| | | | | | | | | | | | | | |
$--GGA,hhmmss.ss,llll.ll,a,yyyyy.yy,a,x,xx,x.x,x.x,M,x.x,M,x.x,xxxx*hh
1) Time (UTC)
2) Latitude
3) N or S (North or South)
4) Longitude
5) E or W (East or West)
6) GPS Quality Indicator,
0 - fix not available,
1 - GPS fix,
2 - Differential GPS fix
7) Number of satellites in view, 00 - 12
8) Horizontal Dilution of precision
9) Antenna Altitude above/below mean-sea-level (geoid)
10) Units of antenna altitude, meters
11) Geoidal separation, the difference between the WGS-84 earth
ellipsoid and mean-sea-level (geoid), "-" means mean-sea-level below ellipsoid
12) Units of geoidal separation, meters
13) Age of differential GPS data, time in seconds since last SC104
type 1 or 9 update, null field when DGPS is not used
14) Differential reference station ID, 0000-1023
15) Checksum